## Slide 1
>_
CS4CS · NETWORKING LAB
Internet Detective
Open a captured network trace and prove how a password leaked. One packet at a time.
>_ Internet Detective · Networking Lab
01
Notes: Welcome them to the practical session after the networking lecture. Everyone opens a simulated packet analyzer in the browser, no installs or logins. Frame it as a forensics case: the packets are evidence, and they are the investigators.

## Slide 2
THE CASE
A laptop on the school Wi-Fi may have leaked a password. We captured every packet it sent. Open the trace and prove what happened.
Mission: find the leak, name how it happened, and say what would have stopped it.
>_ Internet Detective · Networking Lab
02
Notes: Read it like a case briefing. The capture is a real-looking set of packets telling one story. They will follow the evidence to a single packet that proves the leak.

## Slide 3
HOW TODAY WORKS
Before we start
Work solo or in pairs
A pair sharing one laptop is great. Talk through every clue out loud.
Move together
We do one task at a time as a room. Please don't race ahead of the slides.
We're here to help
Stuck for more than a minute? Raise a hand and an instructor will come over.
>_ Internet Detective · Networking Lab
03
Notes: Same rules as the last lab: lockstep. Eight tasks, one at a time. Instructors float and help anyone who falls behind.

## Slide 4
SETUP · OPEN THE LAB
Open the lab in your browser
GO TO THIS LINK
[ paste your lab link here ]
A short link or QR code is easiest for a room of 60. Replace this before class.
What you'll see
A packet analyzer with a filter bar on top, a color-coded list of packets, and a detail pane. Eight tasks sit on the right. Click any packet to open it.
>_ Internet Detective · Networking Lab
04
Notes: Drop your GitHub Pages / Netlify link or a QR code here before class. If wifi flakes, students can open the .html file you shared on Drive, since it runs offline. Give everyone about 2 minutes to load it and confirm they see the packet list.

## Slide 5
THE PACKET ANALYZER
Your toolkit
Filter bar type dns, http, tls, tcp, udp, or an IP to narrow the list. The quick buttons do the same.
Packet list every packet in time order: who sent it, who got it, and the protocol. Colors group them.
Detail pane click a packet to crack it open and read its layers, from the MAC up to the app.
>_ Internet Detective · Networking Lab
05
Notes: Give a 30-second tour live on your screen: filter, list, detail. Show one click so they see a packet open into layers. Then they drive.

## Slide 6
CONNECT TO TODAY'S LECTURE
Everything here is from class
The TCP/IP model every packet you open is the model in action: device → host → app.
Ports and protocols port 53 = DNS, 80 = HTTP, 443 = HTTPS. The port tells you the service.
TCP vs UDP reliable and ordered, or lean and fire-and-forget. You'll meet both today.
Public vs private IP 192.168.x.x is your LAN. Everything else is out on the internet.
>_ Internet Detective · Networking Lab
06
Notes: Tie straight back to the lecture. The phrase 'device to host to app' is the spine of the whole session, so say it out loud here and again at every packet they open.

## Slide 7
TASK 1 OF 8 · NAMES TO NUMBERS
Find the DNS lookups
DO THIS
Type dns in the filter bar and press Enter (or tap the DNS button). Find where a name like free-prize-login.tk is turned into an IP address.
DNS is the phone book
DNS turns a human name into an IP address, on port 53 over UDP. Notice that the bait name resolves to an address out on the internet.
>_ Internet Detective · Networking Lab
07
Notes: They should spot the DNS query/response for free-prize-login.tk resolving to 185.220.101.42. That outside address is the first thread to pull.

## Slide 8
TASK 2 OF 8 · PLAIN TEXT
Find the cleartext HTTP
DO THIS
Filter for http. Open the POST /submit packet sent to free-prize-login.tk and read the form data inside it.
HTTP hides nothing
Plain HTTP on port 80 sends everything readable. This POST carries a username and password in clear text. That is your smoking gun.
>_ Internet Detective · Networking Lab
08
Notes: Answer key: the POST to free-prize-login.tk contains username=j.smith and the password in plain text. Let the room react when they read a password straight off the wire.

## Slide 9
TASK 3 OF 8 · LOCKED VS OPEN
Find the encrypted traffic
DO THIS
Filter for tls. Open a packet to the real school portal at 104.18.22.10 and try to read what is inside it.
HTTPS is the lock
HTTPS on port 443 wraps the data in TLS, so you see only scrambled bytes. Same internet, but the bait site skipped this protection.
>_ Internet Detective · Networking Lab
09
Notes: The contrast is the lesson: the legit portal is encrypted and unreadable, the bait site is plain and exposed. Encryption is the only difference.

## Slide 10
TASK 4 OF 8 · OUTSIDE-IN
Read a packet's layers
DO THIS
Click any packet to open the detail pane. Read it from the outside in: the frame (MAC), then the IP, then the port.
Device to host to app
Each layer wraps the one above. MAC moves it across the local link, IP across networks, the port to the right app. That is the whole model.
>_ Internet Detective · Networking Lab
10
Notes: This is the heart of the lecture made concrete. Have them say the chain out loud: MAC is the device, IP is the host, port is the app.

## Slide 11
TASK 5 OF 8 · RELIABLE
Inspect a TCP packet
DO THIS
Filter for tcp. Open one of the first packets between the laptop and a server and look at the handshake flags.
TCP sets up first
TCP does a three-way handshake (SYN, SYN-ACK, ACK), numbers every byte, and resends what gets lost. Web, email and files ride on it.
>_ Internet Detective · Networking Lab
11
Notes: Point out the handshake. TCP trades a little speed for reliability, which is why anything that must arrive intact uses it.

## Slide 12
TASK 6 OF 8 · FIRE AND FORGET
Inspect a UDP packet
DO THIS
Filter for udp. Open the DNS lookup you found in task 1 and compare it with the TCP packet you just opened.
UDP just sends
UDP has no handshake and no resend. It is lean and fast, which is why DNS, voice and video use it. Speed over guarantees.
>_ Internet Detective · Networking Lab
12
Notes: Side by side: TCP has setup and acknowledgements, UDP just fires. DNS uses UDP because a lookup is tiny and easy to retry.

## Slide 13
TASK 7 OF 8 · LOCAL OR INTERNET
Run the subnet round
DO THIS
Tap the Subnet round button. Sort six addresses into Local (this LAN) or Internet, using 192.168.1.0/24 as the dividing line.
The /24 is the border
A /24 means the first three numbers are the network. So 192.168.1.x is on the LAN, and anything else lives out on the internet, a WAN.
>_ Internet Detective · Networking Lab
13
Notes: Answer key: 192.168.1.105, .1 and .20 are local; 104.18.22.10, 185.220.101.42 and 8.8.8.8 are internet. The /24 keeps the first three octets fixed.

## Slide 14
REFERENCE · ANATOMY OF A PACKET
One frame, three addresses
MAC
Layer 2
→ device (local link)
IP
Layer 3
→ host (across networks)
PORT
Layer 4
→ app (the service)
DATA
Payload
→ your actual message
Read a packet outside-in: MAC, then IP, then port, then the data. Device → host → app.
>_ Internet Detective · Networking Lab
14
Notes: Use this whenever a student is lost in the detail pane. The same four addresses appear on every packet, in this order, from the outside in.

## Slide 15
TASK 8 OF 8 · MAKE THE CALL
Solve the case
DO THIS
Tap Solve the case. Using everything you found, choose what really happened and how the password leaked.
Name it, then fix it
A bait domain resolved to an outside server, the laptop connected over plain HTTP, and the password went out in clear text. HTTPS would have hidden it.
>_ Internet Detective · Networking Lab
15
Notes: Correct answer: phishing site over plain HTTP, credentials sent in cleartext. A correct call marks the final task done and closes the case.

## Slide 16
CASE CLOSED
What the trace showed
1 · The bait DNS resolved free-prize-login.tk to 185.220.101.42, a server out on the internet.
2 · The connection the laptop opened plain HTTP on port 80 to that server, with no encryption.
3 · The leak a POST sent the username and password in clear text for anyone on the path to read.
4 · The fix over HTTPS on port 443 the same data would have been scrambled and safe.
>_ Internet Detective · Networking Lab
16
Notes: Walk the timeline once, in order. This is the story the packets told. Each line maps to a task they just completed.

## Slide 17
THE BIG IDEA
The only difference between a safe login and a leaked one was a single letter: the S in HTTPS.
Encryption turns readable data into nonsense for everyone but the right server.
>_ Internet Detective · Networking Lab
17
Notes: Land it. They will check for the padlock and https on real sites after this. That habit is the takeaway.

## Slide 18
DEBRIEF · TALK IT OUT
Discuss with your partner
The tell
which single packet proved the password leaked, and why?
Defense
what one change would have kept that password secret?
Real world
how can you tell HTTP from HTTPS in your own browser?
>_ Internet Detective · Networking Lab
18
Notes: Give pairs 2 to 3 minutes, then take a few answers. Aim for: the cleartext POST; switch to HTTPS; look for https and the padlock in the address bar.

## Slide 19
GO FURTHER AT HOME
Try the real thing
Real Wireshark
free at wireshark.org. Open a sample capture and explore real traffic the way you did today.
See your own path
look up your public IP, or run tracert to watch your data hop across the internet.
picoCTF
free browser challenges with a networking track. A great next step after today.
>_ Internet Detective · Networking Lab
19
Notes: For the keen ones. Wireshark is the real version of today's tool. Note that ping and tracert may be blocked on school wifi but work fine on home networks.

## Slide 20
NICE WORK
You read real packet structure, told encrypted from plain text, drew the subnet line, and cracked the case. That is network forensics.
Questions?
>_ Internet Detective · Networking Lab
20
Notes: Close out and invite questions. Thank them for following along in lockstep. That wraps the two practical labs.